## Slide 1: Release 1
Motor Control System

## Slide 2: ECU1 System
Check DTC
start
init
Check receiving temp from ECU2
Check system state
flag for receiving a temp from ECU2
Flag for sending acknowledge and wait to be reset by the response of ECU2
Communication Lost flag
OverHeated Flag
Fault flag
ECU1 system control flags
-Global overheat counter
-Global Fault state counter
-Global Comm. Lost counter
Packet to pc [state-temp]

## Slide 3: Check receiving temp from ECU2
start
If ECU1 recevied a temprature
Clear irq flag
Check if temp is ok and not out of range for 3 times
If n_ok
Send frame to inquire for voltage
Receiving the volt
If volt in ragne
Pc_packet = overheat
Fault counter = 0
Overheat counter ++
Overheat irq flag = 1
Fault irq flag = 0
Fault counter ++
Overheat counter = 0
Overheat flag = 0
Fault irq flag = 1
Load pc packet with temp
nothing
Load pc packet with temp.
flag for receiving a temp from ECU2
Flag for sending acknowledge and wait to be reset by the response of ECU2
Communication Lost flag
OverHeated Flag
Fault flag
ECU1 system control flags

## Slide 4: Check system current state [ Normal State or Com. Lost]
start
If all flags are 0 “normal”
Pc packet state = normal
Global com. counter = 0
ack flag = 1 & com. Lost flag = 1
Pc packet state = com. lost
Com. Lost counter ++

## Slide 5: Check using DTC or not
start
If any counter exceed the limit
Check the source
Hault until solved

## Slide 6: Timing Sequences “interrupt based”
Send alive message
Send state to pc “uart”
Check commuinication
500 ms
1 sec
5 sec
System periodic actions
flag for receiving a temp from ECU2
Flag for sending acknowledge and wait to be reset by the response of ECU2
Communication Lost flag
OverHeated Flag
Fault flag
ECU1 system control flags

## Slide 7
[1]Send alive message, 500 ms
start
Send remote frame to ECU2
Set the waiting acknowledge flag

## Slide 8
[2]Send state to pc “1 sec”
start
Send state to uart

## Slide 9
[3]Check communication “5 sec”
start
If waiting for ackhnowledge flag ==1
Set communication lost flag
Clear communication lost flag

## Slide 10: What next:
For ECU1:
- Implement DTC Storing Error in the EEPROM
- upload on the hardware
For ECU2:
- implementing the logic of the ECU2
- Testing the Logic
Release 2 :
Release 3 :
For ECU2 :
- upload on hardware
- test the whole system
Release 4 :
- test the whole system
- documentation